The George Washington University 
 School of Engineering and Applied Science 
 Department of Electrical and Computer Engineering 
 ECE 20 - LAB 
Experiment # 4

Characterization of an NPN Bipolar Junction Transistor (BJT)

Components:

| Kit Part # | Spice Part Name | Part Description | Symbol Name (used in schematics throughout this lab manual) |
| --- | --- | --- | --- |
| 2N3904 | Q2N3904 | NPN Bipolar Junction Transistor (BJT) | Q1 |
| Resistor | R | 100kΩ Resistor | RB |
| Resistor | R | 1kΩ Resistor | RC |

Table 1.1

Objectives:

- To characterize a BJT using the Tektronix Model 571 Curve Tracer

- To characterize the base-emitter pn-junction (BEJ) and base-collector pn-junction (BCJ) of a BJT using the Tektronix Model 571 Curve Tracer

- To characterize a BJT using a Power Supply & Keithley Model 175 DMM

- To compare measured characterization results to manufacturer specifications

Prelab: (Submit electronically prior to lab meeting, also have a printed copy for yourself during lab)

- Read through lab, generate an equipment list.

- Create a table called: Table P.1 with the following cell headings:

| Calculated Values | Simulated Values | Measured Values |
| --- | --- | --- |
| IB | VCE | IC | VBE | βeta | IB | VCE | IC | VBE | βeta | IB | VCC | VCE | IC | VBB | VBE | βeta |

- Build & simulate the circuit in figure P.1 using SPICE

  - Using the “Parametric Sweep Simulation of a BJT” SPICE tutorial on the lab website to generate an IV Curve (IC vs VCE) for the 2N3904 BJT transistor:

  - Sweep VCE from 0 to 10V, in .2V increments

  - Set IB to be the “parameter” and step it from 10μ to 50μA in 20μA steps

  - Use a current probe to plot IC vs. VCE  at each step of IB to generate 3 curves

  - Place markers at VCE=2V on each curve

  - Record the values for: VCE, IC, and IB from the curve markers in Table P.1, the values for VBE will be found in step i)

  - Delete the IC current probe & place a voltage probe at node VB as shown in fig P.2

  - Re-run the same simulation, place markers at VCE=2V on each curve

  - Record the values for: VBE, from the curve markers in Table P.1

  - Calculate the value of the DC current gain (βeta = IC / IB) for each row of table P.1

| Figure P.1- Circuit to generate IC vs. VCE curve (IB curves) | Figure P.2 Circuit to generate IC vs. VCE curve (VBE curves) |
| --- | --- |

- Use equation P.1 to calculate IC and record the values in the “calculated value” section of table P.1

  - Calculate IC for each value of VBE collected in step 3

  - Assume Is=6.734fA, and the typical value for VT ≈ 26mA (thermal voltage)

  - Calculate the value of the DC current gain (βeta = IC / IB) for each row of table P.1

Equation P.1 – Collector Current of NPN BJT in the active region of operation (Assumptions: VA >>VCE and n=1)

- In the simulation above, we have swept VCE from 0 to 10V, and IB from 10μ to 50μA.  But the 2N3904 BJT can handle a significantly higher set of values.  From the specification sheet for the 2N3904 BJT, gather the following specifications:

| Parameter | Value (with units) |
| --- | --- |
| Maximum Collector-Emitter Voltage (VCEO) |  |
| Maximum Emitter-Base Voltage (VEBO) |  |
| Maximum Continuous Collector Current (IC) |  |
| Maximum Collector-Base Voltage (VCBO) |  |
| Maximum DC Current Gain (βeta or hFE) |  |
| Base-Emitter ON Voltage (VBE) when VCE=5V and IC=10mA at room temperature (note: see graph section of spec) |  |

LAB:

Part I – Transistor Characterization using a Curve Tracer:

Generating an IC vs. VCE IV-Curve for the BJT:

- Allow the GTA to demonstrate using the Tektronix Model 571 Curve Tracer for an NPN device.

- Set the Tektronix Model 571 Curve Tracer to generate 3 IV-curves for the 2N3904 Transistor with the following limits:

- Limit IC to be no greater than 10mA

- Set VCE to be swept from 0 to 10V

- Step IB from 10μ to 50μA in 20μA steps to generate the 3 curves

- Print the resulting family of curves, annotate IB on each curve (by hand), and indicate the limits of your setup in the lab write-up.  Be sure to scan the printout into your lab write-up.

Generating the IV-Curve for BEJ and CEJ for the BJT pn-junctions:

- Set the Tektronix Model 571 Curve Tracer to generate the forward IV characteristic curve for the Base-Emitter Junction of the 2N3904 Transistor.

- Determine the limits for the B-E junction using the manufacturer specification sheet as done in lab 1

- Print the resulting curve, indicate the voltage & current limits and scan the printout into your lab write-up

- Set the Tektronix Model 571 Curve Tracer to generate the forward IV characteristic curve for the Base-Collector Junction of the 2N3904 Transistor.

- Determine the limits for the B-E junction using the manufacturer specification sheet as done in lab 1

- Print the resulting curve, indicate the voltage & current limits and scan the printout into your lab write-up

Part II – Transistor Characterization Using a Test Circuit -

Generating the IC vs. VCE family of IV-Curves for a BJT:

In this lab, you will generate only 3 IV-Curves (IC vs. VBE) as you did in the prelab.  IB will be the ‘parameter’ whose value will step from IB=10uA to 50uA in 20uA steps.

In the prelab you generated an IV-Curve for the 2N3904 using the schematic in figure P.1.  You were able to generate base current IB in the range of 0 to 50uA.  In the lab, the power supply can behave as a current source, but it cannot produce a current as small as 50uA.  To create the same family of IV-Curve in the lab, we must use the circuit in figure L.1.  The voltage source combined with the 100kΩ resistor at the base will behave as the 0 to 50uA current source from figure P.1.

The data collected during this section of lab is to be recorded under the “Measured Values” section of Table P.1

Measuring the IB=10uA curve

- Build the circuit depicted in figure L.1 using the 2N3904 BJT

- Measure the exact resistance of RB using the Ohm meter, record this value

- Measure the exact resistance of RC using the Ohm meter, record this value

- Use a DMM to measure the voltage at node VB in the circuit L.1, this is VBE

- Use a DMM to measure the voltage at node VC in the circuit L.1, this is VCE

- Adjust VCC until VCE equals 2V

- Adjust VBB until VBE equals the value found in prelab when IB=10uA & VCE=2V

- Now, readjust VCC until VCE equals 0 V

- Record VCC, VCE, VBB, & VBE in table P.1

- Calculate the voltage across RB to calculated and record current IB in table P.1

- Calculate the voltage across RC to calculated and record current IC in table P.1

- Adjust VCE from 0V to 2V in .2V steps, repeating steps (i)-(k) at each step

- Adjust VCE from 2V to 10V in 1V steps, repeating steps (i)-(k) at each step.

- Calculate βeta for each recorded value of IC and IB

Measuring the IB=30uA curve

- Repeat steps (a)-(n) above, but in step (g) adjust VBB until IB=30uA; you will need to calculate the current IB from the voltage across RB.

Measuring the IB=50uA curve

- Repeat steps (a)-(n) above, but in step (g) adjust VBB until IB=50uA; you will need to calculate the current IB from the voltage across RB.

Figure L.1 – Test circuit to generate family of IV-curves for an NPN BJT

Part III – Data Analysis

- Plot a family of IV-Curves for the data collected for Calculated Values & Measured Values, in table P.1

- Extract a few values for IB, VCE, IC, and VBE from the curve-tracer plots, place these in another set of columns in table P.1

- Compare the Calculated, Simulated, Measured (curve-tracer & keithley measured values) via graphs (overlaying them where possible) and percentage error in all cases.

# Text boxes

IB

IC