The George Washington University 
 School of Engineering and Applied Science 
 Department of Electrical and Computer Engineering 
 ECE 20 - LAB 
Final Project Preparation

Initial Calculations for Final Project &

Characterization of iPod, function generator, and speaker

Objectives:

- Characterize the TIP31A NPN BJT

- Design Architecture for Final Project, implement in SPICE

- Characterize function generator, iPod (or other music source), and speaker

Prelab: (Submit electronically prior to lab meeting, also have a printed copy for yourself during lab)

- Read through lab, generate a components and equipment list.

- From the specification sheet for the TIP31A NPN BJT (on the lab website), gather the following specifications:

| Parameter | Value (with units) |
| --- | --- |
| Maximum Collector-Emitter Voltage (VCEO) |  |
| Maximum Emitter-Base Voltage (VEBO) |  |
| Maximum Continuous Collector Current (IC) |  |
| Maximum Peak Collector Current (IC) |  |
| Maximum Collector-Base Voltage (VCBO) |  |
| Maximum DC Current Gain (βeta or hFE) |  |
| What is the range of βeta (hFE) @25°C– see graph |  |
| What happens to βeta as collector current increases? |  |
| How much base current is required to get 1Amp of collector current? – see graph |  |

- Read the tutorial “Cascading Amplifier Stages (CE to CC)” to help you design an amplifier to meet specifications below

- Design an amplifier using NPN BJTs to meet the following specs (hand in all calculations):

| Specification | Value |
| --- | --- |
| VCC | 12V or 24V (choice is up to student) |
| RL | 8Ω |
| Power dissipated by load | 10Watts RMS |
| vin | .7V RMS @ 10kHz |

  - Show through calculations and specifications for the 2N3904, why the 2N3904 cannot reach the output power goal

  - Can the TIP31A BJT be used to meet the output power goal?  If so, use it to design the common-collector output stage.

    - You will need to generate an IV-curve for the TIP31A to determine the base current the BJT requires (follow the process learned in lab 4 to do this)

    - Looking for the TIP31A part in spice?  Read tutorial: “How to load a new part into spice”

- Build the amplifier you’ve designed in SPICE, use 50 ohms for Rsig.

- Perform a Bias Point Analysis for the circuit.

  - Show the DC voltages and DC currents at each node; submit a separate screenshot for each.  Verify that the DC currents and node voltage approximate your calculations.

- Perform a Transient Analysis, show 5 cycles of:

  - Plot Vin (not vsig), Vout for each stage (use markers to show values)

  - Plot Iout for the CC stage

  - Calculate the voltage gain for each stage

  - Plot Vin, (not vsig), Vout, and peak power out for the entire amplifier (use markers to show values)

  - Calculate the overall voltage gain and current gain for the entire amplifier

Lab:

In your final project you will be asked to design a multistage amplifier for music.  In parts 1-3 we will determine the input or output impedance for the lab function generator, your iPod (or other music source, lab pc perhaps), and an audio speaker.

Part 1 – Determining Output Impedance of the Function Generator

- Set the lab function generator to produce a 2Vpp 440Hz wave

- Attach the output of the function generator to the oscilloscope’s channel 1

  - Measure & record the output voltage of the function generator in the table below

  - Adjust the frequency to 1kHz, then 10kHz record the output voltage at each step

- Set a 100 ohm potentiometer to its maximum resistance, attach it to the function generator as shown in the figure below

  - Set the frequency back to 440Hz

  - Measure the voltage across the potentiometer

  - Adjust the frequency to 1kHz, then 10kHz record the output voltage at each step

- At 440Hz:

  - Adjust the potentiometer until the voltage across the POT = ½ Vout (no load)

  - Detach the potentiometer and measure its resistance (this equals Rsig at 440Hz)

- Repeat step 4a-b for 1kHz, then 10kHz

| Frequency | Vout (peak) (no load) | Vout (peak) (100Ohms) | Vout (peak) | Rsig |
| --- | --- | --- | --- | --- |
| 440 Hz |  |  |  |  |
| 1 kHz |  |  |  |  |
| 10 kHz |  |  |  |  |

Part 2 – Determining Output Impedance of an iPod (or PC’s audio out)

You could use a potentiometer to your iPod’s output, but we don’t want to accidentally short it out and break your iPod, so we will use resistors instead in this section.

- On the iPod, play a 440Hz tone on a loop

- Attach the output of the iPod to the oscilloscope’s channel 1 to measure its Vout

  - Adjust the volume on the iPod until Vout = 2Vpp (record below)

  - Attach a 500kΩ resistor as RL to your iPod’s output, measure Vout across RL

  - Attach a 1kΩ resistor as RL to your iPod’s output, measure Vout across RL

  - Attach a 500Ω resistor as RL to your iPod’s output, measure Vout across RL

  - Attach a 100Ω resistor as RL to your iPod’s output, measure Vout across RL

  - Attach a 75Ω resistor as RL to your iPod’s output, measure Vout across RL

  - Attach a 50Ω resistor as RL to your iPod’s output, measure Vout across RL

  - Attach a 8Ω resistor as RL to your iPod’s output, measure Vout across RL

- Adjust the frequency to 1kHz, then 10kHz record the output voltage at each step

- Calculate Rsig in each case, for each resistor value.

| Frequency | Vout (peak) (no load) | Vout (500 kΩ) | 1kΩ | 500Ω | … |
| --- | --- | --- | --- | --- | --- |
| 440 Hz |  |  |  |  |  |
| 1 kHz |  |  |  |  |  |
| 10 kHz |  |  |  |  |  |

Part 3 – Determining Input Impedance of a speaker

This procedure will be discussed in lab

Analysis

- What is the output impedance of the iPod?

- What is the output impedance of the function generator?

- What is the input impedance of the speaker in your kit?

# Text boxes

+

RL

-

Rsig

Vsig

iPod

(or any music source)

LOAD

RL

POTΩ

Rsig

Vsig

Function generator

LOAD