## Slide 1: ECE 3130 – Digital Electronics and Design
Lab 1
Introduction to Tanner Tools
Fall 2012

## Slide 2: Objectives
Review basic digital circuit concepts
Develop an understanding of digital circuit design and simulation
Learn the basics of the Tanner Tools software

## Slide 3: How do digital circuits work?
Analog – continuous signal
Digital – discrete signal
Fundamentally binary devices
Quantization of voltage
  HIGH
  LOW

## Slide 4: Generic Voltage Transfer Characteristics
Input
  IN ≤ VIL  “0”
  IN ≥ VIH  “1”
Output
  OUT ≤ VOL  “0”
  OUT ≥ VOH  “1”

## Slide 5: Propagation Delay (tP)
When the gate inputs change, the outputs do not change instantaneously
Defined as the latency between a change in the input and a change in the output measured from the 50% point at the input and the 50% point at the output
tPHL – the time it takes for the output to switch from HIGH to LOW
tPLH – the time it takes for the output to switch from LOW to HIGH

## Slide 6: Logic Gates
AND
OR
NOT (a.k.a. inverter)
NAND
NOR
XOR
XNOR

## Slide 7: Introduction to MOSFETS
Four terminal devices
  Gate
  Source
  Drain
  Body
Two types
  PMOS – source connected to VHIGH
  NMOS – source connected to VLOW
*NOTE*: The body is always shorted to the source in both devices

## Slide 8: Tanner Tools Components
5 Modules
  L-Edit
  LVS
  S-Edit
  T-Spice
  W-Edit

## Slide 9: Let’s Start…
Start  All Programs  Tanner EDA  Tanner Tools v15.0  S-Edit v15.0 64-bit

## Slide 10
This is the startup interface

## Slide 11
Make a new design file

## Slide 12
Name the design
Create a directory to store your files and set the path

## Slide 13
Make a new cell

## Slide 14
Name the cell and select schematic

## Slide 15
This is the schematic workspace

## Slide 16
Add the following libraries:
C:\Users\Student\Documents\Tanner EDA\Tanner Tools v15.0\Process\Generic_250nm\Generic_250nm_Devices\Generic_250nm_Devices.tanner
C:\Users\Student\Documents\Tanner EDA\Tanner Tools v15.0\Process\Standard_Libraries\Misc\Misc.tanner

## Slide 17: Inverter
Truth table
Implementation
Input | Output
0 | 1
1 | 0

## Slide 18
Select the devices library
Select the desire component from the parts list
Press “Instance”

## Slide 19
Left-click to place on grid then click Done
Select 4T

## Slide 20
Vdd and Gnd are found in the Misc library
Wire
In
Out

## Slide 21
Now let’s make a symbol for the inverter

## Slide 22
Select the same cell as your schematic
Select “symbol” from view
Click OK

## Slide 23
This is the symbol workspace.
Let’s have Tanner generate a symbol for us.

## Slide 24
Make sure the Design and Cell are correct and then hit “Replace”

## Slide 25
This is the auto-generated symbol but let’s make it better.
Pick the Pointer tool, select the box, and press Backspace to delete it
Pointer

## Slide 26
Pick the “Path” tool and “All angle” selection
Draw the standard logic symbol for an inverter
Draw “paths” to connect everything
All angle
Path

## Slide 27: Building the Test Bench
Make new design file
Call it inverter_test
Add the inverter library, which you just made
Add the following libraries
  C:\Users\Student\Documents\Tanner EDA\Tanner Tools v15.0\Process\Standard_Libraries\SPICE_Commands\SPICE_Commands.tanner
  C:\Users\Student\Documents\Tanner EDA\Tanner Tools v15.0\Process\Standard_Libraries\SPICE_Elements\SPICE_Elements.tanner

## Slide 28
Voltage source is found in the SPICE_Elements library
Print Voltage is found in the SPICE_Commands library
Capacitor is found in the Devices library
Voltage source (pulse)

## Slide 29
C:\Users\Student\Documents\Tanner EDA\Tanner Tools v15.0\Process\Generic_250nm\Generic_250nm_Tech\Generic_250nm.lib TT
Press this button to set up the simulation

## Slide 30
Set the stop time and maximum time step and hit Run Simulation

## Slide 32: NAND Gate
Truth table
Implementation
A | B | Output
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 36: Analysis
Tabulate the propagation delays (tPHL, tPLH) for the inverter and NAND gate.
Record the waveforms.