## Slide 1: ECE 3130 – Digital Electronics and Design
Lab 2
Adders and Multiplexers
Fall 2012

## Slide 2: Objectives
Learn how adders and multiplexers work
Build and simulate a half and full adder
Build and simulate a 2-to-1 and 4-to-1 multiplexer

## Slide 3: What are adders?
Digital circuits that perform addition of numbers
Half adder
  Adds two 1-bit binary numbers
Full adder
  Adds three 1-bit binary numbers

## Slide 4: Half Adder
Truth table
Implementation
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 5: Full Adder
Truth table
A | B | C | Sum | Carry
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 6: Full Adder Implementation
Implementation

## Slide 7: Analysis
In addition to the truth table, include the Boolean equation for the sum and carry of the half and full adder.
Report, in tabular form, the propagation delays (tPHL, tPLH) of the sum and carry for the half adder.
Which output has longer delay: sum or carry? Can you say why?

## Slide 8: What is a multiplexer (MUX)?
A device with multiple inputs and one output
Also known as a data selector or controlled switch

## Slide 9: How does it work?
A MUX has n select lines, 2n inputs and 1 output
The select line chooses which input to pass to the output
2-to-1 MUX
Truth table
S | A | B | Z
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 10: 2:1 MUX Gate Implementation

## Slide 11: 4-to-1 MUX
Truth table
S1 | S2 | Output (M)
0 | 0 | A
0 | 1 | B
1 | 0 | C
1 | 1 | D

## Slide 12: Homework
Build a 2:1 MUX and simulate it
Build a 4:1 MUX from your 2:1 MUX (hint: you will need three 2:1 MUX’s) and simulate it
You will be using the 4:1 MUX next lab